Material/Component	Bulk		Bagged		Palleted	Packaged	Loose

Sand	-

Gravel	-

Hardcore	-

Ashes	-

Spoil	-

Topsoil	-

Turves					-

Cement	-	-	-*

Concrete	-

Structural timber					-

Joinery sections				-	-

Trusses			-*	-	-

Sheet timber			-*	-	-

Precast concrete			-		-

Steel reinforcement			-*	-	-

Metal windows					-

Steel sections					-

Bricks			-*	-	-

Blocks			-	-	-

Plaster	-	-	-*

Plasterboard			-*		-

Service pipes				-	-

Sanitary fittings					-

Kitchen fittings					-

Nails				-

Screws				-

Ironmongery				-	-

Drainage pipes			-*		-

Ceiling tiles				-

Floor tiles				-

Curbs			-*		-

Paving slabs					-

Doors			-*	-	-

Seaffolding					-

Seraffold fittings				-	-

Electrical fittings				-

Radiators					-

*shows where a material or component can be delivered in a form suitable for mechanical offloading

Storate of Materials

| Mateial | Likely damage | Effects of weather | Methods of storage | Type of protection |
| --- | --- | --- | --- | --- |
| Bricks facings | chipping on face and corners breakage, effects of mud slashes | saturation from rain, possible frost damage, excesively dry from solar radiation | in neat stacks max height 1.8m on even platform | top and half way down the sides covered by waterproof sheeting well secured, also sheet ground and sides if in muddy conditions |
| commons | chipping of face and corners breakage, effects of mud slashes | saturation from rain, possible frost damage, excessively dry from solar radiation | in neat stacks max height 1.8m on even platform | not absolutely necessary |
| Blocks clinker | brekage | saturation from rain possible frost damage, excessively dry from solar radiation | in neat stacks max height 1.8m on even platform | top and half way down the sides covered by waterproof sheeting well secured |
| concrete | breakage | very little out varies with density | in neat stacks max height 1.8 m on even platform | top and half way down the sides covered by waterproof sheeting well secured |
| clay hollow blocks | breakage | saturation by rain, possible frost damage | in neat stacks max height 1.8m on even platform | top and half way down, ie. sides covered by waterproof sheeting well secured |
| Cement bagged | broken bags causing spillage | cement hardening in damp atmosphere | in stacks max height 2 m on even platform off ground, ensure oldest bags used first | placed in a closed shed with large doors for easy access, allow for ventilation to maintain a dry atmosphere |

| Mateial | Likely damage | Effects of weather | Methods of storage | Type of protection |
| --- | --- | --- | --- | --- |
| Cement (continued) bulk | spilage | cement hardening and gorming lumps in damp atmosphere | in purpose made silo | adequate protection afforded by the silo |
| Plaster bagged | broken bags causing spillage | plaster hardening and forming lumps in damp atmosphere | in stacks max height 2m on even platform off the ground, ensure oldest plaster used before commencing latest delivery | preferably within the building alternatively completely covered over with well secured waterproofed sheeting |
| Plasterboard | fracture of sheets corners damaged | saturation by rain brings disintegration | in stacks laid horizontally max height 2m on a continuous even platform | fully covered with well secured waterproof sheeting prefereably taken into building as soon as possible |
| Timber joists | twisting, wraping, bowing | saturation by rain | in next stacks laid horizontally on an even platform | waterproof sheet over leaving ends uncovered. |
| roof trusses | twisting, warping, bowing | saturation by rain | in neat stacks laid horizontally on an even platform, but even platform, but stacks not to exceed 12 in number | water proof sheet over leaving ends uncovered, but allow for adequate ventilation |

| Mateial | Likely damage | Effects of weather | Methods of storage | Type of protection |
| --- | --- | --- | --- | --- |
| Timber (continued) flooring boards | twisting, warping, bowing | saturation by rain | in neat stacks laid horizontally on an even platform off the ground using spacing laths | waterproof sheet over leaving ends uncovered, but allow for adequate ventilation |
| chipboard | fracture, damage at corners | saturation by rain brings about disintegration | in neat stacks laid horizontally on an even platform off the ground using spacing laths | preferably within the building, if external fully |
| joinery sections | fracture, twisting, warping, bowing | saturation by rain | in well constructed racks off the ground laid horizontally | top and sides covered with waterproof sheeting, ends left open for ventilation and access, ensure timber is |
| fabricated units | fracture, twisting, warping, bowing | saturation by rain | stacked vertically against a strong support on runners | fully covered with waterproof sheeting well secured but allowing some ventilation |
| doors and door sets | face markings, winding | saturation by rain | door sets stacked vertically as above, doors vertically or horizontally if on an even base, classify in sizes and types | in an enclosed shed having a dry atmosphere and handling room, must be lockable |
| Metal copper tubes | buckles | only over a long period of time | in racks giving adequate lateral support | in a shed with fully security |

| Mateial | Likely damage | Effects of weather | Methods of storage | Type of protection |
| --- | --- | --- | --- | --- |
| Metal (continued) cast iron pipe | fracture | rusting over a long period of time | in racks, for large diameters use wedges or shaped timbers to prevent rolling | no protection required if stored in a compound |
| sheet metals | bent and mishapen scratching to applied finish | very little effect | in stacks laid horizontally on an even platform off the ground | protective membrane between sheets |
| fabricated units | breakages to fittings and buckling | very little effect | veritically against a strong support on a platform or runners | galvanised and aluminium units to be kept clear of ashes as these will corrode |
| ironmongery | breakage of fittings, loss by theft | rusting of small steel parts | in bins or shelves classified in sets or types | located in a full security shed for maximum protection |
| Sundries sanitary ware | brekage of fitting, chipping and cracking | little or no effect in the short term | separately on an even base | preferably placed at point of use within the building |
| plastic goods | breakage, buckling, crushing | some plastics effected by solar radiation | in racks with adequate lateral support | protection from pilfering |
| screws and nails | loss by pilfering | rusting | in strong boxes or bins according to size | in a central location with security |
| kitchen fittings | twisting, warping, facial marking | saturation by rain | in stacks max 2 units high on an even base | in a shed with adequate access or direct to point of use in the building |

| Mateial | Likely damage | Effects of weather | Methods of storage | Type of protection |
| --- | --- | --- | --- | --- |
| Sundries (continued) precast concrete panels | breakage, facila markings, chipping to arrises | no effect | predominately vertical on strong purpose made raked racks, depends upon position of lifting hooks | protection to corners to prevent chipping, refer to handling instructions |
| precast concrete floor beams | breakages and cracking | no effect (water can lie in the hollows within the beams) | stacked horizontally off the ground with timber spaces | little required |
| sand gravel gravel | none | saturated with rain, frozen in frost, contaminated with spoil, etc | on hard flat base with some form of enclosure to prevent spreading | covered to preven excess water content and give protection from frost |
| lime sand | none | saturated with rain, frozen in frost, contaminated with spoin, etc. but also solar radiation | on hard flat base with some form of enclosure to prevent spreading | covered to prevent excess water content and give protection from frost and excessive drying |
| steel reinforcement | bent out of shape | slight rusting | on hard flat base on timber runners | none required |
| scaffolding | buckling | rusting to steel tubes and fittings | in racks according to length or in contained stacks on runners | fittings well greased before use |

Appendix 1   Schedule of Materials Controls

| Mateial | Handling | Storage | Protection | Loss or Waste |
| --- | --- | --- | --- | --- |
| Topsoil | Bulldozer or scraper box to storage areas Strip with mechanical plant Load into trucks Remove to storage areas | In mounds not exceeding 1.8 m high | Avoid storing or discharging chemical or deleterious matter adjacent to topsoil mounds | Strip taken too deep / too shallow Storing in excessive mounds Indiscriminate handling Double handling |
| Hardcore | Delivere in high-sided trucks Tip close to point required Transfer by mechanical shovel Place in layers Consolidate with roller | In mounds as required | Must be free of timber, plaster, metal and chemical waste | Over-excavation will require additonal hardcore Using for unspecified areas, temporary roads, low-lying areas etc |
| Fine and coarse aggregates | Delivered by high-sided truck Check quality, grade and quantity Tip into prepared bays or selected areas Transfer by grab, mechanical shovel or opwr-assisted equipment on weigh batcher Transport by bucket, hopper, dumper and barrow | In prepared bays adjacent to mixer in selected grading and particle size On concrete base laid to falls | Cover against frost, snow or rain Avoid contamination with mud, clay or oil Install steam heating to base of mound Check calibrations on weighing equipment | Indiscriminate handling Contamination of any kind Failure to trim stocks Using as site dressing or to fill site voids |

| Mateial | Handling | Storage | Protection | Loss or Waste |
| --- | --- | --- | --- | --- |
| Cement | Delivered by tanker and pumped into silo Delivered in 50 kg paper sacks on timber pallets Offload by forklift or crane Use bagged cement in order of delivery | In special silo adjacent to mixer On raised platforms in shed or in open Covered completely with tarpaulin or polythene sheet | Avoid accidental bursting of sacks Restrict rising moisture affecting cement in store Cover against rain, snow and ice | Humidity causing materials for lump Dampaness initiating set Indiscriminate handling causing bags to burst Failure to use deliveries in rotation Pilfering Leaving stocks unused |
| Concrete | By crane, skip, hopper, dumper or barrow Special site truck fitted with paddle agitator Transfer by concrete pump from delivery to placing point Ready-mixed concrete delivered by special truck capable of mixing en route Ensure good access roads to discharge pointor hoisting areaa | In special hoppers or skips when transferring to upper levels On suitably sized timber or metal sheets with side supports to restrict concrete spreading | Avoid mud or other deterious matter affecting concrete, at any stage Cover where necessary to restrict rain, snow or frost affecting mix Use heated water for mixing in low temperature | Overloading containers Overestimating quantity required Late delivery of ready-mixed concrete Failure to plan work in hand Mix not to specification Carless placing Unspecified use of concrte |
| Formwork | Clean formwork between operations Remove all nails and screws Keep formwork together including bolts and fixings Hoist with care Do not drop formwork when stripping from concrete | Arrange formwork in sections for identification Lay flat where possible Stack vertically where necessary Protect edges and | Avoid damage from site traffic Maintain reasonable moisture content in timber formwork Oil and clean metal formwork Avoid ice gathering on formwork | Mishandling formwork when stripping from concrete Dropping bolts or fixings in mud Using formwork for other purposes Failing to retrice formwork where backfill |

| Mateial | Handling | Storage | Protection | Loss or Waste |
| --- | --- | --- | --- | --- |
| Reinforcement | Offload as close to fixing point as possible Lay on timber skids to keep steel above ground Check type and quantity delivered Cut with proper tools Use correct size mandrels for bending bars Do not heat bars when bending steel Hoist bundles of bars or sheet reinforcement with care | Mat reinforcement to be laid flat Bar reinforcement to be stored in racks Separeate bent bars into types according to Bending Schedule Retain all offcuts | Guard agains oil, mud or loose scale on steel Avoid distortion of bars by site traffic or mishandling | Careless handling Leaving bars behind in fixing areas Failing to fix steel as specified Cutting bars incorrectly Leaving offcuts in mud |
| DPCs | Unroll quantity to be used only Replace surplus amounts in safe storage Use proper knife for cutting to length Use correct width as specified | Store in cool, dry place Do not stack rolls on side Keep different widths in separate groups | Avoid head affecting rolls Store away from site traffic Do not drop rolls, where damage will result | Leaving unused rolls lying around Using incorrect widths or cutting unnecessarily |
| Polythene sheeting | Unroll only as required Cut off and weight down Use sharp knife and straight edge when cutting | Keep out of bright sunshine Support rolls throughout lengths Keep different gauges apart | Avoid foot traffic etc over sheet when laid Keep heat away from sheeting Avoid damage with reinforcement sheets or bars | Caused with careless handling Using wrong gauge where lesser thickness specified Unspecified use of sheets eg. as protection for materials etc. |

| Mateial | Handling | Storage | Protection | Loss or Waste |
| --- | --- | --- | --- | --- |
|  | Delivered in packs or on pallets Offload by vehicle-crane, forlkift or mobile crane Transfer on site by forklift, dumper, crane, hoist or elevator Sort all chipped or damaged bricks and set aside Do not tip facing bricks Cut bands holding packs with proper cutters | In selected stock-piles adjacent to work in progress On prepared base of hardcore, concrete or ash Store according to type Keep stacks within reasonable height | Guard against undiscriminate handling methods Avoid chipping to arrises and face Mud splashes to base of stack Cover stacks to protect against rain, snow, frost Contamination from soluble salts or sulphates | Using facings for common work or as supports and packings Faulty workmanship Double handling |
| Blocks | Delivered on pallets or in polythene-covered pecks Offloard by vehicle-crane, forklift or mobile crane Transfer on site by forklift, crane etc Keep stacks secure: not too high | Keep different types separate Stack on prepared base Do not form stacks more than three packs high | Avoid tipping blocks from dumper Use packs up before opening otheres Avoid contamination with mud or sulphates | Using blocks as packings Excess breakages |
| Mortar | Delivered in premix loads either In bulk or containers Transport on site in skips, dumper, barrow, mortar trays Use forklift, hoist or crane Offload close to work areas | In containers or in for adding cement Deposit bulk deliveries on suitable timber, metal sheet, or concrete base having side supports to prevent | Avoid contamination by mud or other deleterious matter Cover with sheet to prevent rain, snow or frost affecting the materials Guard against excess use of plasticiser | Incorrect mix pro portions Overloading transport vehicle Over estimating quantities required Deliberate disposal of |

| Mateial | Handling | Storage | Protection | Loss or Waste |
| --- | --- | --- | --- | --- |
| Precast items | Offload and transport with care using correct equipment and any lifting points provided in the casting Protect edges where slings or cables used for fitting Lifting equipment to be fully capable of raising the load | Stack on level base according to size and type Use softwood bearers placed at equally spaced centres Wall panels stacked vertically in special frames Store units with steel in lowre section Store close to fixing area where possible | Cover stocks to avoid impact damage Sheet over to avoid weathering from rain, snow or ice Projecting reinforcement should be covered to avoid rust stains to units | Damaged or broken units will be expensive to replace; repeated orders cost money Duplication of items mean waste Shortages of items mean waste Shortages of p.c. items can create delays |
| Metal ties and fixing brackets | Wall ties to be built in as work proceeds Brackets should be fixed to frames with screws before building in All brackets and ties should be retained in areas here used and surplus collected and returned to store | Store in bundles on wire and issue in proportionate amounts for work in progress | Ties etc. must be protected from rust or corrosion Avoid placing in line of site traffic Do not leave in muddy areas | Over-issue causes waste Materials left around after completion of work in danger of being lost Even loss of small items can add up to major expenditur4e on large contracts |

| Mateial | Handling | Storage | Protection | Loss or Waste |
| --- | --- | --- | --- | --- |
| Carecassing | Delivered by supplier Offload by contractor using forklift or mobile crane Distribution on site by trailer Delivered in graded sizes to meet orders | Form stacks on skids to raise above ground Form one fair end to stack Provide spacers to ensure continuous airflow around timber Stack timbers according to type and cross-section | Should be treated off site with vacuum-impregnation of salts to give protection against rod Maintain stacks in tidy condition and stockpiles in suitable areas where they will not be contaminated with mud, plaster or cement Covers required to avoid rain, snow or ice affecting timber | Mainly through inaccurate cutting and disposal of offcuts Using wrong type and cross-sections of timber Inadequate protection against site traffic |
| Timber sheeting | Delivered in packs Offload by forklift Handle individual boards on edge | Place packs on skids or bearers Ensure stack is fully supported Store different types of board in separate stacks | Store under cover Edges to be safeguarded against impact Cover with waterproof sheet when not in store | Indiscriminate cutting of sheets Poor stacking causing boards to warp Pilfering Using for unspecified purposes |
| Trussed | Delivered in banded lots Offload by mobile crane Lift with truss in vertical position Lifting points should be at caves joint Mechanical handling required for raising banded sets to roof level | Stack vertically with support where wall-plate bearing occurs Ends of rafter must be clear of ground Where stacked horizontally, trusses should be retained in banded lots on | Provide good support in storage Care essential with joints Avoid strain on joints when lifting Cover required to keep off rain, snow or ice | Damaged joints are unacceptable therefore truss is written off Impact when hoisting causes damage Dropping truss either at roof or ground level also creates damage Careless storage |

| Mateial | Handling | Storage | Protection | Loss or Waste |
| --- | --- | --- | --- | --- |
| Flooring boards | Delivered by supplier Offload and stack Transfer to fixing areas in quantities required | Stack horizontally on bearers using spacers between packs Stack boards in triangular pattern where space available Check moisture content | Place under cover or use waterproof sheets Keep ends open to provide air flow around boards | Misuse in handling Poor stacking Impact damage Cutting patterns Twisting or bowing |
| Joinery | Delivered as required Support fully when offloading or transferring on site Protect ends or returns when hoisting or moving | Must be stored under cover to maintain specified moisture content Full support required to joints and offsets Ensure airflow around items Mouldings etc to be in racks | Wrap projections with sacking to avoid impact damage Cover against rain, snow or ice Apply suitable primer where specifiied as soon as possible after manufacture | Special items will be written off if damaged Delay to contract with need for replacements |
| Door and window frames | Delivered by manufacturer Offload by contractor Stack carefully in compound Transfer to working area required for fixing | Frames to be laid flat where possible and fully supported particularly at joints Placed on bearers to raise off groun Stack in groups according to type | Primed as soon as possible after manufacture Where frames have been pressure-treated they should be allowed good air circulation before priming | Damaged frames |

| Mateial | Handling | Storage | Protection | Loss or Waste |
| --- | --- | --- | --- | --- |
| Doors | Delivered in large loads Check quantities Offload by contractor Door and doorset may be on pallets Use forklift for offloading Site trailer and hoist for distribution | Store in area wher e temperature not likely to produce sudden changes Doors laid flat on timber platform or stacked vertically Arrange in lots according to size and thickness Doorsets laid flat should have ‘pull’ side uppermost Stack under cover at all times | Where polythene covers to door these remain until ready for application of door finish Prime hardboard doors on delivery Store in locked premises | Poor stacking causes bowing or twisting Damp conditions can affect joints and glue Theft likely Damage generally results in total loss |
| Nails, bolts and screws | Delivered in boxes and sacks Issue in plastic bags in correct quantities and sizes Return surplus to store | Use boxes and bins to retain different sizes etc | Retain in dry storage to avoid corrosion | Indiscriminate use on site Depositing in muddy areas; where nails etc fall they are rarely retrieved |
| Roof felt | Delivered by platform vehicle Offloaded manually To upper levels by forklift mobile hoist or elevator hoist Distributed at roof level Do not overload roof by slacking felt in one place Use sharp knife for cutting to | Stack rolls on end in a cool part of compound Avoid stacking rolls on top of each other Stack in groups according to grade and quality | Cover against hot sunshine Clean off roof before laying Clean off between layers Punch home all nails before laying felt | Generally through faulty handling Dropping rolls and part rolls from root level Damage to ends when stacking rolls Unspecified uses on site |

| Mateial | Handling | Storage | Protection | Loss or Waste |
| --- | --- | --- | --- | --- |
| Roof tiles and slates | Delivered by supplier Offloaded manually unless in packs Care in handling to avoid breakages | Stored in rows on flat base adjacent to work area Arrange in sizes where random slating involved | Stack clear of traffic routes Keep well back from road intersections where vehicles are liable to cut the corner Crawl board should be used on finished roof | Mishandling materials at all stages Damage from site traffic |
| Plaster | Delivered on platform vehicle in 40 kg and 50 kg paper sacks, and on pallets 2 tonnes in weight Offload by forklift or manually Distribute by dumper or site trailer | In building where used or in prepared sheds Stacks in groups according to type Keep stacks low to avoid weight on lower bags Use bags in rotation | Keep bags covered to avoid moisture afecting the plaster Use burst bags first if no lumpiness present Keep storage area clean | Lumps forming in bags mean it should not be used Leaving stocks over two months can result in waste as moisture is absorbed by plaster |

| Mateial | Handling | Storage | Protection | Loss or Waste |
| --- | --- | --- | --- | --- |
| Plasterboard | Delivered by supplier in platform base vehicles Offloaded by forklift; requires platform to support the boards Manual handling and stacking requires two men to each board Plastic or foil-backed boards should be handled with reverse face to face | Boards should be stacked on a level surface in dry condition Boards should be stored in a suitable building If stored externally they should be raised above the ground on a timber platform and completely covered with waterproof sheeting Stacks should not exceed 900 mm. Where stacks on concrete floor, polythene sheet should be laid under the boards and returned up to protect the edges | Avoid damage to surface or edge of boards Boards should nto be dragged over each other Stack away from site traffic runs | Using wrong size boards causing excess cutting Poor stacking Indiscriminate handling Lack of protection from weather |
| Glass | Delivered on specially equipped vehicles Offload by glaziers Size of pane and type of glass affect handling procedures Large panes carried by slings or special suction pads with handles Edges of glass should be | Store must be clean and dry Lay glass on edge in racks with felt-or rubber-covered base Galss to be fully supported with bearers at right-angles to glass | Full support required to avoid sheet bending Guard against any impact Avoid splashes of cement or plaster; cleaning down may create surface scratches Mark glazed areas with whitening or plastic stickers | Scratches cause waste Brekages Leaching Inaccurate cutting Faulty glazing |

| Mateial | Handling | Storage | Protection | Loss or Waste |
| --- | --- | --- | --- | --- |
| Putty and mastics | Delivered by supplier in drums Do not use turps in putty to make workable Keep different materials separate | Store on racks on staging Avoid extreme temperatures Keep lids firmly closed Issue materials in correct quantities Keep separate drum for surplus returned | Follow manufacturers’ directions for use Guard against frost and rain Pilfering Use by other trades | Use for specified purposes only Leaving drums open Using too much material for glazing purposes |
| Ironmongery fittings | Receive from supplier in boxes Issues to operatives as required for work in progress Make up into complete sets for issue to operatives Return surplus to store each day | Stock in shelving or in bins where easily accessible Ensure types easily identified | Where paper or polythene film on door or window furniture this should remain until completion of contract Keep all items in locked store Issue items against official schedules only | Theft from store or after fixing Careless issuing from stores Poor accounting Failing to return surplus to store |
| Tanks and cylinders | Offload and transfer to store with care Check protective measures have been applied where specified Place into position at correct stages of progress | Stock in suitable sector of compound to aovid impact damage Avoid other materials being retained within tanks Do not store in unlocked buildings | Where cutting holes for pipe connections ensure treatment of bare metal Clean out all metal filings from tanks and cylinders Support base of tank with timber platform Avoid plaster droppings into tanks and cylinders | Damage to cylinders causing rejections |

| Mateial | Handling | Storage | Protection | Loss or Waste |
| --- | --- | --- | --- | --- |
| Radiatorsm taps and fittings | Delivered in plastics wrapping or in crates Check quantities and type Stack radiators according to size | Keep in dry conditions Catalogue type in stock Produce ‘sets’ for issue to operatives | Gaurd against rust to radiators Only issue quantities shown in schedules Surplus returned to stores each day | Poor accounting Pilfering Damage after fixing |
| Sanitary-ware and fittings | Delivered by supplier Offload by contractor directly into store Check quantities delivered Deliver items to working area and store inside locked buildings | Retain in racks or on platforms Keep smaller items in cartons Do not stack units too high Avoid items projecting into route of site traffic | Maintain protective covering of making tape Avoid chipping to glazed surfaces Impact can create hairline cracks Over-tightening unions etc can cause cracks later as items expand with hot water Avoid film of plaster or cement on glazed surfaces | Damage to these items inevitably means they are written off Check carefully on completion to avoid subsequent claim for breakages |
| Plastic and copper pipes | Delivered in lengths or in rolls Checks quantities and type of materials particularly gauge of pipe Offload directly etc | Store in racks within locked accommodation Retain pipes in accordance with type of material Protect plastic pipe from heat to avoid distortion | Check quantity issued each time Avoid materials being left lying on site Ensure subsequent damage unlikely after fixing Use correct equipment for bending copper pipes | Damage by site traffic Damage after fixing Theft Frost damage Vandalism Using wrong gauge of pipe |

| Mateial | Handling | Storage | Protection | Loss or Waste |
| --- | --- | --- | --- | --- |
| Plastic-faced floor coverings | Delivered by manufacturer Offload and store by fixers where available Applicaiton only to dry sub-floors | Store in cool dry conditions Retain tile finishes in cartons Place sheet flooring on racks | Cover materials against impact before and after laying Check sub-floor before fixing to avoid sulphate or acid attack | Cutting incorrectly |
| Gutters and rainwater pipes | Fix as work proceeds to avoid damage to structure Check angles, offsets and bends each section when commenced | Store in racks in compound Keep plastic gutters etc away from heat sources Form components in separate stacks according to type Keep fittings in boxes or crates | Avoid impact damage Do not leave work partly fixed Provide light waterproof covers to stack Plastic components must be stored with support to length of pipe gutter | Pilfering Damage by site traffic Vandalism Failure to collect surplus lengths and fittings Plastic materials brittle in low temperature |
| Cast iron drainage | Delivered and offloaded by manufacturer/supplier Handle pipes with care Keep clear of mud, cement and plaster | Place on skids with bearers across length to avoid movement of stack Do not over stack | Site so as to avoid damage to collars or spigot end Provide cover against rain, snow and ice | Breakages Incorrect cutting |

| Mateial | Handling | Storage | Protection | Loss or Waste |
| --- | --- | --- | --- | --- |
| Salt-glazed drainage | Delivered and offloaded by manufacturer/supplier Care required in transferring materials on site Check quality and quantities Return surplus pipes and fittings to store | Offload onto firm even base close to working area Store in compound or well back from traffic route Pipes retained in packs or stacked on bearers Fittings retained in separate area away from site traffic | Secure stacks by wedging batten along bottom row Spigots fitted with polyester moulding Stacked with spigot projecting in alternate courses | Leakages Storage Overgrown with weed Careless handling |
| Paints | Offload directly into store Don’t open tins indiscriminately Replace lids securely after use Apply from kettles not the tin Do not mix different brands | Place tins on racks in well ventilated dry store Keep different paints in specific grouping Display NO SMOKING signs Keep store clean | Avoid extreme temperature Don’t use thinners excessively Seal cans and tins after use | Poor storage Poor distribution Leaving surplus in kettle |